## Slide 1: How to build HiFive1 demo using Freefom Studio
Nov-19-2019

## Slide 2: Software requirement
Freedom Studio
  FreedomStudio-2019-08-1-win64.zip
Demo source code
  freertos-code-r2752-trunk_SHC_demo.7z

## Slide 3: Freedom Studio
Go to https://www.sifive.com/boards
Download Freedom Studio and extract it
  (This document use FreedomStudio-2019-08-1-win64.zip)

## Slide 4: Edit PATH variable for Freedom Studio
Open System Properties
Select Environment Variables... > User variables > Path
Click Edit…
Add new value to PATH
  Example in this manual
  E:\AWS-FreeRTOS-HiFive1\FreedomStudio-2019-08-1-win64\SiFive\riscv64-unknown-elf-gcc-8.3.0-2019.08.0
  E:\AWS-FreeRTOS-HiFive1\FreedomStudio-2019-08-1-win64\SiFive\riscv64-unknown-elf-gcc-8.3.0-2019.08.0\bin
  E:\AWS-FreeRTOS-HiFive1\FreedomStudio-2019-08-1-win64\SiFive\msys64-1.0.0-2019.05.2\usr\bin
Click OK

## Slide 5: HiFive1 demo
Extract Workspace_FreeRTOS_HiFive1.7z
Create a new folder named Workspace

## Slide 6: Build HiFive1 demo
Run FreedomStudio and navigate to Workspace

## Slide 7: Import Project
In Menu select File > Import
Select General > Existing Projects into Workspace
Click Next

## Slide 8: Import Project
Choose Select root directory
Click Browse… and navigate to freertos-code-r2752-trunk_SHC_demo directory
Note: Do not check in Copy projects into workspace
Click Finish

## Slide 9: Build HiFive1 demo
Select RTOSDemo and build project

## Slide 10: Add new debug configuration
After building finished, connect HiFive1 board to your PC
Right click to project, select Debug As > Debug Configurations …
In Debug Configurations window, select Sifive GDB SEGGER J-Link Debugging
Right click and select New Configuration

## Slide 11: Debug configurations
Project: RTOSDemo
C/C++ Applicaton: Debug\RTOSDemo

## Slide 12: Debug configurations
DTS File: bsp\design.dts
Actual path:
  Example:
  E:\AWS-FreeRTOS-HiFive1\freertos-code-r2752-trunk_SHC_demo\FreeRTOS\Demo\RISC-V_RV32_SiFive_HiFive1_FreedomStudio\bsp\design.dts
Selected cpu: cpu@0

## Slide 13: Debug configurations
Device name: FE310
Click Debug and wait to flash binary on board

## Slide 14: Run HiFive1 demo
Select Terminate to stop Debug
Press RESET button on HiFive1 board to run demo

## Slide 15: View print log
Use terminal as TeraTerm (baud rate = 115200) to see log

## Slide 16: Build error
Refer to slide 4 “Edit PATH variable for Freedom Studio” if see this error